## Slide 1: PoE Product Training
Instructor Name

## Slide 2
Topics
Introduction to PoE
TRENDnet PoE Products
  802.3at or PoE+
  802.3af standard PoE
  Splitters/Injectors
  IP Cameras
  Wireless Access Points
Applications
TRENDnet Advantage
Questions

## Slide 3
Introduction
What is Power over Ethernet (PoE)?
  PoE technology describes any system that transmits electrical power, in addition to data, to remote devices over standard twisted-pair wire in an Ethernet network.

## Slide 4
Introduction
How is Power over Ethernet (PoE) used?
  PoE is useful for powering IP telephones, wireless LAN access points, IP cameras, and other low power network appliances where it would be inconvenient or infeasible to supply power separately.
Power + Data

## Slide 5
Introduction
Features
Industry Standard
  IEEE 802.3at = 34.2 watts (PoE+)
  IEEE 802.3af = 15.4 watts (PoE)
Cabling
  Cat 5,5e,or 6 Ethernet Cable
Common Applications
  Wireless Devices
  Internet Cameras
  VoIP Phones

## Slide 6
The Three Elements of PoE
  Power Sourcing Equipment (PSE)
  Powered Device (PD)
  Patch
TPE-114GS (Splitter)
TPE-115GI (Injector)
TEW-753DAP
TV-IP302PI
TPE-224WS
TPE-TG44G
TPE-1620WS
TPE-T80H
TPE-104GS (Splitter)
Introduction
TV-IP450PI
TPE-TG160g

## Slide 7
Power Sourcing Equipment (PSE)
  The PSE is connected to a device and at once detects whether the device falls into two categories. It's either a compliant device or it's non-compliant. If the device is compliant with the 802.3af or 802.3at standard then adequate power is supplied. If the device is non-compliant then power is not supplied.
  These devices are designed to detect the power needed by providing a range of voltage from 37 up to 57 Volts to supply the necessary power levels to each device automatically.
Introduction

## Slide 8
Powered Device (PD)
  This is your VoIP Phone, camera, Wi-Fi access point or other devices. This will provide the correct impedance to the PSE and ideally send a signal to the PSE indicating how much power it requires.
  Devices that are true 802.3af or 802.3at only need a single interface for power and data via the same network cabling.
  Non-Compliant PoE can use a splitter to achieve that same advantages as standardized devices.
Introduction

## Slide 9
Cabling
  CAT 5 cable or better is used to transmit the power. The advantage is that this commonly used Ethernet cables can be used to keep installation costs down. The maximum length of cable is 100m (328ft) and the delivered power is 30w for PoE+ and 15.4w for standard PoE.
Introduction

## Slide 10
Cabling – PoE+ Repeaters
Introduction

## Slide 11
Introduction
PoE Power Up Stages

## Slide 12
Benefits
Cost Saving - reducing costs of new power outlets
Mobility - allows you a variety of setups without being tied down to a power outlet
Management – Ability to provide and control power output to specific devices.
Introduction

## Slide 13
Model | PoE Port | PoE Power Consumption | Features
TV-IP572(P/PI) | (1x) 10/100Mbps (802.3af) | 3.15W/4.95W | Megapixel/ H.264 572PI is IR
TV-IP612P | (1x) 10/100Mbps (802.3af) | 12W | Optical Zoom
TV-IP672(P/PI) | (1x) 10/100Mbps (802.3af) | 9W | PTZ/Megapixel 672PI is IR
TV-IP252P | (1x) 10/100Mbps (802.3af) | 8W | Fixed Dome
TV-IP262PI | (1x) 10/100Mbps (802.3af) | 7W | Megapixel/H.264
PoE IP Cameras

## Slide 14
PoE IP Cameras
Model | PoE Port | PoE Power Consumption | Features
TV-IP311PI | (1x) 10/100Mbps (802.3af) | 5W | 3 Megapixel resolution ONVIF
TV-IP302P1 | (1x) 10/100Mbps (802.3af) | 6.24W | Wide angle Megapixel/H.264
TV-IP322P | (1x) 10/100Mbps (802.3af) | 9.5W | Narrow field of vision Megapixel/H.264
TV-IP310PI | (1x) 10/100Mbps (802.3af) | 5W | 3 Megapixel resolution ONVIF
TV-IP430PI | (1x) 10/100Mbps PoE + (802.3at) | 20W | 2 Megapixel/H.264 ONVIF v2.2
TV-IP450PI | (1x) 10/100Mbps PoE + (802.3at) | 35W | Megapixel/H.264 ONVIF v2.2

## Slide 15
Model | Fast Ethernet | Gigabit | PoE Splitter Voltage/Wattage | PoE Injector Power Output
TPE-103I |  |  | N/A | 802.3af (mode A) Pins: 1, 2, 3, 6
TPE-104S |  |  | 5V, 7.5V, 9V, 12V | N/A
TPE-113GI |  |  | N/A | 802.3af (mode A) Pins: 1, 2, 3, 6
TPE-114GS |  |  | 5V, 7.5V, 9V, 12V | N/A
TPE-115GI |  |  | N/A | 802.3at (mode A) Pins: 1, 2, 3, 6
TPE-105I |  |  | N/A | 802.3at (mode A) Pins: 1, 2, 3, 6
Splitters/Injectors

## Slide 16
Model | Ports | IEEE PoE Standards | Total PoE Power Output | Unmanaged Plug & Play Design
TPE-TG44G | 4x (PoE/PoE+) 4x(Non-PoE) 10/100/1000Mbps | 802.3af 802.3at | 60 Watts (4x15w or 2x30w) | 
TPE-T80* | 8x (PoE/PoE+) 10/100Mbps | 802.3af 802.3at | 240 Watts (8x30w) | 
TPE-TG80G | 8x (PoE/PoE+) 10/100/1000Mbps | 802.3af 802.3at | 105 Watts (7x15w or 3x30w) | 
TPE-TG81G | 8x (PoE/PoE+) 10/100/1000Mbps Rackmount | 802.3af 802.3at | 105 Watts (7x15w or 3x30w) | 
TPE-T88G | 8x (PoE) 8x(Non-PoE) 10/100/1000Mbps | 802.3af 802.3at | 120W (8x 15w or 4x30w) | 
TPE-T160* | 16x (PoE/PoE+) 10/100Mbps | 802.3af 802.3at | 480W (16 x 30w) | 
802.3at or PoE +

## Slide 17
Model | Ports | 10/100/100Mbps Ports | Total PoE Power Output | Web GUI Management
TPE-S44 | 4x (PoE/PoE+) 4x(Non-PoE) 10/100Mbps | NONE | 30W (Aggregate on 4 PoE Ports) | 
TPE-S80 | 8x (PoE) 10/100Mbps | NONE | 126W (8 x 15w) | 
TPE-S160 | 16x (PoE) 10/100Mbps | NONE | 254W (16 x 15w) | 
TPE-1020WS | 8x (PoE/PoE+) 2x(Non-PoE) 10/100/1000Mbps 2 SFP | 10x | 75W (Aggregate on 8 PoE Ports) | 
TPE-1620WS | 16x (PoE/PoE+) 10/100/1000Mbps 2 SFP | 16x | 185W (Aggregate on 16 PoE Ports | 
TPE-224WS | 24x (PoE) 4x (PoE+) 10/100Mbps 2 SFP 4x 1000Mbps | NONE | 193W (Aggregate on 24 PoE Ports) | 
802.3af/at

## Slide 18
Model | Ports | 10/100/100Mbps Ports | Total PoE Power Output | Web GUI Management
TPE-TG240g | 24x (PoE/PoE+) Gigabit | NONE | 370W | 
TPE-2840WS | 4x (PoE+) 20x (PoE) Gigabit 4 SFP | NONE | 185W | 
TPE-4840WS | 12x (PoE+) 12x (PoE) Gigabit 4 SFP Shared | 24x 1000Mbps | 370W | 
802.3af/at

## Slide 19
Model | PoE Port | Speed | PoE Power Consumption | Features
TEW-638PAP | (1x) 10/100Mbps (802.3af) | N300 | 3.12w | 2 2dBi detachable antennas
TEW-753DAP | (1x) 10/100Mbps (802.3af) | N300 Per Band | 12w | Dual band 4dBi antenna VLAN tag support
TEW-735AP | (1x) 10/100Mbps (802.3af) | N300 | 6w | 2 4dBi Antennas Plenum rated VLAN tag support
TEW-653AP | (1x) 10/100Mbps (802.3af) | N300 | 6w | 4dBi Antenna VLAN tag support
802.3af/at

## Slide 20
Total PoE power for entire switch
Some or all ports support PoE
Total power cannot exceeded budget
PoE Power Budget

## Slide 21
Example – TPE-224WS
  24 ports, 15.4W per port, 170W budget
If all PoE devices use 15.4W
  170W / 15.4W = 11 PoE devices supported
Lower PoE requirement = more devices
PoE Power Budget

## Slide 22
PoE Power Budget Calculator
Coming soon…

## Slide 23
TPE-1620WS

## Slide 24
GUI

## Slide 25
GUI
672 = 9W Max
735 = 6W Max

## Slide 26
GUI

## Slide 27
GUI

## Slide 28
TPE-224WS

## Slide 29
TPE-224WS
GUI

## Slide 30
TPE-224WS
GUI

## Slide 31
TPE-224WS
GUI

## Slide 32
PoE Ethernet Switch
(TPE-224WS)
Category 5e Cable
48V DC Power + Ethernet Data
Wireless AP
(TEW-653AP)
Applications

## Slide 33
PoE Switch with Power Splitter
PoE Ethernet Switch
(TPE-224WS)
Category 5e Cable
PoE Power Splitter
(TPE-114GS)
12V DC Power
Ethernet Data (Cat. 5e)
Ethernet Device
(TEW-650AP)
7.5V DC Power
Ethernet Data (Cat. 5e)
48V DC Power + Ethernet Data
Applications

## Slide 34
Power Injector and Powered Device
TEG-224WS
Ethernet Data (Cat. 5e)
PoE Power Injector
(TPE-113GI)
Category 5e Cable
48V DC Power
Ethernet Data (Cat. 5e)
48V DC Power + Ethernet Data
Wireless AP HotSpot
(TEW-638PAP)
Applications

## Slide 35
Power Injector and Power Splitter
TEG-2248WS
Ethernet Data (Cat. 5e)
PoE Power Injector
(TPE-113GI)
Category 5e Cable
PoE Power Splitter
(TPE-114GS)
5V DC Power
Internet Camera
(TV-IP551WI)
48V DC Power
Ethernet Data (Cat. 5e)
48V DC Power + Ethernet Data
5V DC Power
Applications

## Slide 36
Why TRENDnet?
High quality products
Award winning performance
20 years in the business
Advanced product feature sets
Price to performance leadership
Advantage

## Slide 37
Questions?
Q&A

## Slide 38
Thank You

## Slide 39: Agenda
01
Technology Overview
02
TRENDnet Product
03
TRENDnet Product
04
TRENDnet Product
05
TRENDnet Product
06
TRENDnet Product
07
Summary

## Slide 40: Product Definition
Describe the product or service being marketed

## Slide 41: Competition
The competitive landscape
  Provide an overview of product competitors, and their strengths and weaknesses
  Position each competitor’s product against the new product

## Slide 42: Positioning
Positioning of product or service
  Statement that distinctly defines the product in its market and against its competition over time
Consumer promise
  Statement summarizing the benefit of the product or service to the consumer

## Slide 43: Communication Strategies
Messaging by audience
Target consumer demographics

## Slide 44: Packaging and Fulfillment
Product packaging
  Discuss form factor, pricing, look, and strategy
  Discuss fulfillment issues for items not shipped directly with the product
COGs
  Summarize cost of goods and high-level bill of materials

## Slide 45: Launch Strategies
Launch plan
  If product is being announced
Promotion budget
Supply backup material with detailed budget information for review

## Slide 46: Public Relations
Strategy and execution
  PR strategies
  PR plan highlights
  Have backup PR plan including editorial calendars, speaking engagements, conference schedules, etc.

## Slide 47: Advertising
Strategy and execution
  Overview of strategy
  Overview of media and timing
  Overview of ad spending

## Slide 48: Other Promotion
Direct marketing
  Overview of strategy, vehicles, and timing
  Overview of response targets, goals, and budget
Third-party marketing
  Co-marketing arrangements with other companies
Marketing programs
  Other promotional programs

## Slide 49: Pricing
Pricing
  Summarize specific pricing or pricing strategies
  Compare to similar products
Policies
  Summarize policy relevant to understanding key pricing issues

## Slide 50: Distribution
Distribution strategy
Channels of distribution
  Summarize channels of distribution
Distribution by channel
Show plan of what percent share of distribution will be contributed by each channel – a pie chart might be helpful

## Slide 51: Vertical Markets/Segments
Vertical market opportunities
  Discuss specific market segment opportunities
  Address distribution strategies for those markets or segments
  Address use of third-party partner role in distribution to vertical markets

## Slide 52: International
International distribution
  Address distribution strategies
  Discuss issues specific to international distribution
International pricing strategy
Localization issues
  Highlight requirements for local product variations

## Slide 53: Success Metrics
First year goals
Additional year goals
Measures of success/failure
Requirements for success

## Slide 54: Schedule
18-month schedule highlights
Timing
  Isolate timing dependencies critical to success